## Slide 1: Charts That Don't Lie
WEEK 1 · DAY 2
The same data can tell the truth or tell a lie. Learn to draw the truth.
Publica
Academy
Notes: Warm-up: what is a time series? Why .asfreq()?

## Slide 2: Today's mission: three moves
Catch the lie
the average hid every outage
Compare 6 zones
small multiples + index
Tell the story
a title + 4 sentences
10 min hook · 30 min slides · 60 min hands-on · 20 min wrap-up
Notes: Three moves.

## Slide 3: “No Signal” during heavy rain
Heavy rain soaks up the satellite signal: that's rain fade
Ka-band suffers it most. Did our link go down in August, and would our charts show it?
Notes: Everybody has seen DStv drop in a downpour.

## Slide 4: The average lies
PART 1
One month of hourly Ka-band link data
Notes: Section break.

## Slide 5: rf_link_quality_hourly: 744 hours of August
Rain
rain_rate_mmhr: rain at the earth station
Signal quality
cn_ratio_db: carrier-to-noise
Uplink power
uplink_power_dbm: how loud we transmit
Link margin
link_margin_db: below 0 dB = link DOWN
Notes: Link margin is like fuel above the reserve line.

## Slide 6: Same data, two daily summaries
Daily AVERAGE: never below 4.91 dB
Chart: 
| 1 Aug | 8 Aug | 15 Aug | 22 Aug | 29 Aug
value | 5.23 | 5.63 | 5.7 | 5.49 | 5.73 | 5.71 | 5.65 | 5.46 | 5.53 | 5.75 | 5.67 | 5.75 | 5.74 | 5.26 | 5.74 | 5.4 | 5.25 | 5.73 | 5.73 | 5.36 | 5.57 | 5.44 | 5.38 | 5.43 | 5.72 | 4.91 | 5.33 | 5.65 | 5.64 | 5.38 | 5.77
Daily MINIMUM: 11 of 31 days below 0 dB
Chart: 
| 1 Aug | 8 Aug | 15 Aug | 22 Aug | 29 Aug
value | -4.13 | 3.74 | 4.76 | 0.08 | 5.38 | 5.31 | 4.04 | -0.91 | 2.07 | 5.64 | 4.83 | 5.09 | 5.65 | -0.39 | 5.65 | -1.63 | -0.93 | 5.64 | 5.34 | 0.03 | 3.02 | -1.3 | -1.78 | -0.49 | 5.23 | -4.29 | -1.65 | 4.12 | 3.67 | -0.67 | 5.65
Notes: The average says zero outages. The minimum shows the truth.

## Slide 7: “Did we breach?” → plot the worst moment
Daily minimum
SLA, outages: “did it ever go down?”
Daily average
typical level, long-term trend. It hides short outages
Notes: Third Mainland Bridge: average traffic was fine, tell that to the man stuck for 3 hours.

## Slide 8: Uplink power rises because it rains
Rain vs uplink power: correlation 0.97
Uplink averages 41.2 dBm when dry, 44.1 dBm in rain. It's a response, not a second problem. Two units? Two stacked charts, never two y-axes.
Notes: Uplink power control reacts to rain.

## Slide 9: Six zones, one picture
PART 2
VSAT uptime by geopolitical zone, weekly
Notes: Section break.

## Slide 10: Long format → pivot → wide format
# long: 312 rows (52 weeks x 6 zones)
vsat = pd.read_csv(data_path("vsat_uptime_by_region_weekly"),
parse_dates=["week_start"])
# wide: 52 rows x 6 zone columns
wide = vsat.pivot(index="week_start",
columns="region",
values="uptime_pct")
Charts want one column per line: pivot does the reshaping
Notes: Long is how databases export.

## Slide 11: Average uptime by zone: South South is lowest
Chart: 
| North West | North East | North Central | South West | South East | South South
value | 98.93 | 98.25 | 99.12 | 99.1 | 98.59 | 97.67
Tight axis (97–99.5%) because uptime lives near the top: range stated
Notes: In the notebook they draw small multiples on a shared y-axis.

## Slide 12: Indexed to week 1: who fell furthest from their own normal?
Chart: 
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
North West | 100 | 99.93 | 100.21 | 100.11 | 99.93 | 100.1 | 100.07 | 100.06 | 100.05 | 100.22 | 100.21 | 100.16 | 100.1 | 100.05 | 100.02 | 100.15 | 99.96 | 99.96 | 100.22 | 100.14 | 100.18 | 100.05 | 100.07 | 99.82 | 99.9 | 99.65 | 99.85 | 99.74 | 99.65 | 99.4 | 99.61 | 99.5 | 99.33 | 99.57 | 99.62 | 99.35 | 99.54 | 99.54 | 99.57 | 99.74 | 99.61 | 99.82 | 99.92 | 99.88 | 100.12 | 100.04 | 100.23 | 100.15 | 99.96 | 100.06 | 100.09 | 100.18
North East | 100 | 99.96 | 100.05 | 100.19 | 99.99 | 99.9 | 100.22 | 100.23 | 100.24 | 100.2 | 100.22 | 100.11 | 99.99 | 100.08 | 100.23 | 100.16 | 99.98 | 100.04 | 100.08 | 100.23 | 100.06 | 99.9 | 100 | 99.92 | 99.93 | 99.76 | 99.84 | 99.79 | 99.67 | 99.47 | 99.45 | 99.6 | 99.58 | 99.32 | 99.46 | 99.52 | 99.37 | 99.66 | 99.66 | 99.71 | 99.66 | 99.63 | 100.01 | 100.05 | 99.87 | 99.92 | 100.21 | 100.19 | 100.1 | 100.15 | 100.2 | 100.13
North Central | 100 | 99.93 | 100.21 | 100.08 | 99.92 | 99.94 | 100.2 | 99.89 | 99.93 | 100.02 | 99.96 | 100.04 | 100.13 | 99.95 | 99.96 | 100.21 | 99.91 | 99.94 | 99.93 | 100.02 | 100.07 | 100.13 | 99.84 | 99.84 | 99.7 | 99.76 | 99.83 | 99.79 | 99.6 | 99.7 | 99.66 | 99.64 | 99.62 | 99.49 | 99.61 | 99.62 | 99.5 | 99.39 | 99.5 | 99.83 | 99.58 | 99.63 | 99.7 | 99.8 | 99.94 | 100.17 | 100.16 | 100.21 | 100.16 | 100.09 | 100.01 | 99.96
South West | 100 | 99.78 | 100.01 | 99.81 | 99.77 | 100.02 | 99.8 | 99.88 | 99.86 | 99.84 | 100.04 | 99.92 | 99.78 | 100 | 100.04 | 99.85 | 99.78 | 99.97 | 99.93 | 99.85 | 99.86 | 99.97 | 99.86 | 99.71 | 99.45 | 99.24 | 99.16 | 98.82 | 98.8 | 98.48 | 98.4 | 98.26 | 98.45 | 98.35 | 98.33 | 98.54 | 98.63 | 98.55 | 98.88 | 98.85 | 99.15 | 99.15 | 99.41 | 99.34 | 99.84 | 99.94 | 99.9 | 99.91 | 99.82 | 99.92 | 100.05 | 99.79
South East | 100 | 99.95 | 99.97 | 99.81 | 99.81 | 99.83 | 99.76 | 100.02 | 100.02 | 99.88 | 99.73 | 99.84 | 99.8 | 99.92 | 99.88 | 99.93 | 100.01 | 99.92 | 99.78 | 99.94 | 99.83 | 99.68 | 99.82 | 99.36 | 99.19 | 99.11 | 99.03 | 98.83 | 98.8 | 98.73 | 98.41 | 98.54 | 98.22 | 98.43 | 98.28 | 98.27 | 98.53 | 98.45 | 98.76 | 99.01 | 99.06 | 99.15 | 99.33 | 99.65 | 99.72 | 99.68 | 99.99 | 99.99 | 100.03 | 99.73 | 99.92 | 99.93
South South | 100 | 100.18 | 100.29 | 99.96 | 100.14 | 100.01 | 100.21 | 100.11 | 100.01 | 100.16 | 100.22 | 100.12 | 100.24 | 99.94 | 100.16 | 100.08 | 100.11 | 100.11 | 100.08 | 99.99 | 100.2 | 99.97 | 99.82 | 99.89 | 99.76 | 99.32 | 99.23 | 98.95 | 98.88 | 98.72 | 98.58 | 98.75 | 98.58 | 98.59 | 98.61 | 98.67 | 98.54 | 98.84 | 99.07 | 99.14 | 99.14 | 99.46 | 99.65 | 99.63 | 100.01 | 100.05 | 99.94 | 100.2 | 100.22 | 100.09 | 99.95 | 100.17
Notes: South East fell furthest, to 98.2.

## Slide 13: Two questions, two different answers
Question | Chart | Answer
Who is worst? | raw uptime, small multiples | South South (avg 97.67%, worst week 96.56%)
Who dropped most from normal? | indexed to week 1 = 100 | South East (fell to 98.2)
Lowest score is not the same as biggest drop since last term
Notes: Both answers are right. They answer different questions.

## Slide 14: Honest-chart rules
PART 3
Five habits that make charts trustworthy
Notes: Section break.

## Slide 15: Where should the y-axis start?
Percentages near the top
Zoom in (e.g. 96–100%) and write the range on the chart
Counts you can add up
Start at zero, or small differences look huge
Notes: Quiz question 1.

## Slide 16: The 5 honest-chart rules
Threshold line
Title = finding
Sensible axis
One y-axis
Units
Notes: Evidence in court: the other lawyer checks all five.

## Slide 17: A title should state the finding
Names the data
Link margin, August
States the finding
Ka-band link went down on 11 of 31 August days, all during heavy rain
Notes: Quiz question 5.

## Slide 18: The 4-sentence finding
1
Situation: what the unit does
2
Observation: what the data showed, with a number
3
Implication: why it matters
4
Recommendation: what to do next (always LAST)
Notes: Quiz question 6: recommendation comes last.

## Slide 19: Your turn: 60 minutes
1
Open W1D2-exercise in Colab, then Save a copy in Drive
2
Run STEP 0, then top to bottom
3
Part A: catch the average in its lie
4
Part B: six zones, one honest picture
Notes: Walk the room.

## Slide 20: What you now know
Breach questions → plot the minimum, not the average
Many groups → small multiples on one axis; change → index to week 1
Title states the finding; 4 sentences end with the recommendation
Next: Calm Down the Noise (rolling windows)
Notes: Tease Day 3.