## Slide 1: Alarms That Cry Wolf
WEEK 3 · DAY 1
From today we ask: when is a reading wrong?
Publica
Academy
Notes: Welcome to the anomaly-detection half. Today: the alarms we already have, why they cry wolf, and context.

## Slide 2: Today's mission: three moves
Meet your alarm
a fixed limit is already a model
Watch it cry wolf
46 eclipse nights, all alarms
Give it context
same limit, 4 alarms, all real
10 min hook · 30 min slides · 60 min hands-on · 20 min wrap-up
Notes: Three moves.

## Slide 3: November 2008: NigComSat-1 goes silent
Solar-array anomaly
not enough power
Satellite lost
about four years without one
Watch the array
today's main character
Notes: Real history from the fact sheet. Our data is synthetic, the stakes are real.

## Slide 4: The alarm you already have
PART 1
A fixed limit is already a model
Notes: Section break.

## Slide 5: Your NOC already does anomaly detection
if reading < limit:
raise_alarm() # this is a model!
It has a rule, it has a number, and it can be wrong
Notes: Quiz: a threshold is a model (True).

## Slide 6: Four tricks alarm software already knows
Yellow & red limits
warning first, then alarm
Persistence
alarm only if bad for N readings
Hysteresis
on at one level, off at another
State-based limits
different normal per mode
Notes: Each trick buys quiet and can make you blind.

## Slide 7: “Where did that number come from?”
Weak answers
The vendor manual. The old satellite. Oga set it. Nobody knows.
Good answers
Design margin with a reason. Mean ± 3σ of normal data. Reviewed every season.
Notes: Ask it of every limit in your unit.

## Slide 8: Watch it cry wolf
PART 2
Eclipse season
Notes: Section break.

## Slide 9: Every night at 21:00 UTC the satellite runs on battery
Chart: 
46 eclipse hours, 1 Sep to 16 Oct: the satellite's own 'NEPA took light'
Notes: Normal physics, every year.

## Slide 10: Array current below 20 A: 50 alarms
The vendor floor, on all 120 days
50
alarms in total
46
normal eclipse nights
4
real dropouts
8%
of alarms are real
Notes: Every alarm technically correct, operationally useless. SoC < 82% fires 18 times, all eclipse.

## Slide 11: Alarm fatigue
Too many wolves = no shepherd
The car alarm that goes off for every keke: when the real thief comes, nobody moves
Notes: Which alarms in your unit does everyone ignore?

## Slide 12: The fix: add context, don't widen the limit
too_low = bus["solar_array_current_a"] < 20
sunlit = bus["eclipse_flag"] == 0
smart_alarm = too_low & sunlit
# 50 alarms -> 4 alarms, all real
Ask 'which mode is the satellite in?' before checking the limit
Notes: Conditioning on state.

## Slide 13: Battery temp above 22 °C: same trap
Recharging warms the pack for an hour after each eclipse
50
alarms
46
the hour after eclipse
4
left after context
Notes: The remaining 4 are the same solar-array dropout hours.

## Slide 14: Where should the limit be?
PART 3
Let the data choose
Notes: Section break.

## Slide 15: The faults you want to catch widen your own limits
All sunlit hours: σ = 0.59 A
Band 26.43–29.99 A catches exactly the 4 dropouts
Clean hours only: σ = 0.17 A
Band 27.65–28.66 A: 143 alarms, 138 normal recharge hours
Notes: Normal needs context. Day 2 builds it properly. Original says sigma ≈ 0.06; data says 0.59.

## Slide 16: Raining is not the same as link down
August: 56 rainy hours, 12 real outages
18
alarms: 3σ from all hours
12
of them real
49
alarms: 3σ from dry hours
12
of them real
Notes: Link margin below 0 dB = down. Rain alone is not a fault.

## Slide 17: The persistence trick, tested
“Only alarm after 2 hours” catches 0 of 12 outages
Every August outage lasted exactly one hour
Notes: Persistence buys quiet by going blind.

## Slide 18: Uplink power is a reaction to rain: it leaks the answer
Heavy rain
the cause
Signal fades
C/N drops
Power control
41.2 → 44.1 dBm (r = 0.97)
Notes: Quiz: don't feed uplink_power_dbm to the detector.

## Slide 19: Three shapes of trouble
Spike
a limit catches it, with context
Level shift
+2.2 °C: fixed limit fires 0 times
Drift
103 → 95.4 Ah: a 95 Ah limit fires 0 times
Notes: Silent degradation. Days 2 and 3 fix these.

## Slide 20: Your turn: 60 minutes
1
Open W3D1-exercise in Colab and save a copy
2
Part A: count the wolves, add context
3
Part B: let the data choose the limit
4
Part C: rain, delays, leaks and the 3 shapes
Notes: Walk the room.

## Slide 21: What you now know
A limit is a model: ask where every number came from
Add context, don't widen: eclipse, recharge and rain are normal states
Fixed limits catch spikes, not level shifts or slow drift
Next: Control Charts and Residuals
Notes: Tease Day 2.