## Slide 1: Control Charts and Residuals
WEEK 3 · DAY 2
Learn what normal looks like, then flag what leaves it
Publica
Academy
Notes: Yesterday fixed alarms cried wolf. Today the data sets the limits.

## Slide 2: Mama Put knows the price of tomatoes
Know the normal range, and the strange price jumps out
A control chart is that market instinct, written down
Notes: Ask how anyone knows a price is too high.

## Slide 3: Control charts
PART 1
Centre line, two limits, and the discipline to leave normal alone
Notes: Section break.

## Slide 4: Three lines, learned from a quiet stretch
Centre line
mean of a known-good reference period
UCL
centre + 3σ
LCL
centre − 3σ (not min/max, not design limits)
Notes: Control limits = 3 standard deviations either side of the reference-period mean.

## Slide 5: Reference period: 1–15 August
Solar-array current, sunlit, before the eclipse season
360
hours
27.87 A
centre line
0.073 A
σ (normal wobble)
27.65–28.09
control limits (A)
Notes: Original code book's 0.06 A only holds for a clean fortnight. All sunlit hours: 0.594 A.

## Slide 6: Daily lowest current: dropouts fall through the floor
Chart: 
Notes: Three days drop to about 15 A, roughly half the normal output. Lowest: 15.34 A.

## Slide 7: Why 3σ: false alarms in 2,880 normal hours
Chart: 
| ±2σ | ±3σ
value | 131 | 8
Theory on normal data. On our bus data with rolling limits: ±2σ fires 31 times, ±3σ fires 5.
Notes: About 8 false alarms at 3 sigma, about 130 at 2 sigma.

## Slide 8: One satellite, three operating states
Chart: 
| eclipse | sunlit | recharge
value | 0.02 | 28.14 | 29.59
Separate limits per state. Mixing them grows σ from 0.073 A to 0.594 A.
Notes: Fix false alarms with one set of limits per state, not wider limits or deleting data.

## Slide 9: A fixed reference goes stale
Chart: 
Notes: 1,861 of 2,696 sunlit hours outside the August limits: the normal level climbs with the season.

## Slide 10: Rolling limits, robust statistics
Mean + σ: 1.08 A
Right after a dropout hour the rolling σ explodes. One wild point poisons the ruler
Median + MAD: 0.09 A
Barely moves. Trailing 7-day rolling limits give 5 flags: 4 dropouts + 1 false alarm
Notes: MAD × 1.4826 makes it comparable to a standard deviation.

## Slide 11: Common cause, special cause, tampering
Common cause
everyday wobble inside the band: leave it
Special cause
outside the band or a strange run: investigate
Tampering
reacting to normal wobble: spread grows ~39%
Notes: Reacting to common-cause variation as if it were special cause is tampering.

## Slide 12: Run rules
Rule 1: one point beyond 3σ
catches spikes and dropouts
Rule 2: nine in a row
all on one side of the centre: catches level shifts (tomorrow: CUSUM)
Notes: Run rule 2 is most sensitive to level shifts.

## Slide 13: Residuals
PART 2
Not “is it big?” but “is it surprising?”
Notes: Section break.

## Slide 14: Residual = observed − expected
Observed
today's amplifier temperature
Expected
recipe: drive level + time of year
Residual
flag it if bigger than 3σ
Dear tomatoes in the scarce season: expected. Dear tomatoes in a glut: surprise.
Notes: Residual is observed minus expected.

## Slide 15: Amplifier temperature: raw vs residual
Raw: the 68.2 °C spike stays under the 69.8 °C ceiling
Chart: 
Residual: the spike is 23σ; every day after 12 May is high
Chart: 
Notes: Residual σ 0.22 °C vs raw σ 1.97 °C.

## Slide 16: Is the residual clean?
Recipe | Mean | Lag-1 autocorr | Spread H1 / H2
Fitted on all of 2024 | 0.00 | 0.33 | 0.22 / 0.49
Refit without the 2 spike days | 0.00 | 0.06 | 0.22 / 0.22
Checks: mean near zero · no autocorrelation left · constant spread. Never “all above zero”.
Notes: Two bad days in the training data spoiled the recipe.

## Slide 17: Three shapes of trouble
Spike
residuals catch it (23σ)
Level shift
fixed recipe: 233/233 days. Rolling: 0 flags
Slow drift
rolling residual: useless. Tomorrow: CUSUM
Notes: Centred windows also swallow part of a spike and peek at the future. Trailing only.

## Slide 18: Your turn: 60 minutes
1
Open W3D2-exercise in Colab
2
File → Save a copy in Drive
3
Run STEP 0, then top to bottom
4
Replace every ___, run, get the green tick
Notes: Walk the room.

## Slide 19: What you now know
Control chart: centre ± 3σ, one set of limits per operating state, keep it fresh
Robust: median + MAD × 1.4826; never tamper with common-cause wobble
Residual = observed − expected; check it's clean; weak on slow drift
Next: The Slow Creep: Drift and CUSUM
Notes: Tease W3D3.