## Slide 1: The Slow Creep: Drift and CUSUM
WEEK 3 · DAY 3
Some faults never shout. Build a detector that keeps the receipts
Publica
Academy
Notes: Today: faults that creep. By the end everyone writes a CUSUM detector.

## Slide 2: Today's mission: three moves
See what 3σ misses
the amplifier's sneaky step
Build CUSUM
add up small leftovers
Watch the slope
a battery ageing faster
10 min hook · 30 min slides · 60 min hands-on · 20 min wrap-up + project checkpoint
Notes: Three moves.

## Slide 3: The landlord's “small-small” increases add up
Chart: 
| Year 1 | Year 2 | Year 3 | Year 4 | Year 5 | Year 6
rent (₦k) | 500 | 525 | 550 | 580 | 610 | 650
Illustration: ₦415k extra over 6 years. CUSUM keeps the receipts
Notes: No single year shocks you. Adding up the extras does.

## Slide 4: Three shapes of trouble
Spike
one reading way off, then back
Level shift
a step to a new level that holds
Drift
a slow lean: the slope changes
Notes: Days 1–2 caught spikes. Today: shifts and drifts.

## Slide 5: Amplifier temperature: a 3σ rule fires 0 times
Chart: 
Daily 3σ ceiling 69.8 °C, hottest day 68.15 °C: never crossed. The step from 12 May 2025 hides in the yearly swing
Notes: Global mean 63.90, sd 1.97.

## Slide 6: Zoom in: 30 days before vs after 12 May 2025
Against its neighbours it's a giant. Against the whole two years, a dwarf
65.20
°C average before
67.37
°C average after
6.9σ
jump vs local wobble (0.32)
1.1σ
jump vs whole series
Notes: Quiz: no single reading looks extreme against the whole series.

## Slide 7: Step 1: take away what you already know
Actual
the reading
Expected
drive + sun angle + ageing, learned from 2024
Leftovers
σ = 0.20 °C; after the step: +1.83
Notes: Residual = actual minus expected.

## Slide 8: Step 2: the CUSUM line
def cusum(values, k):
S, out = 0, []
for x in values:
S = max(0, S + x - k) # add leftover, minus slack, never below 0
out.append(S)
return out
Alarm when S goes above h. k = 0.5σ (slack), h = 5σ (evidence)
Notes: Quiz: CUSUM accumulates small deviations so a sustained change becomes a clear slope.

## Slide 9: By hand: k = 0.5, h = 2.0
Day | Leftover | S
Day 1 | +0.3 | 0.0
Day 2 | -0.2 | 0.0
Day 3 | +0.4 | 0.0
Day 4 | +1.0 | 0.5
Day 5 | +1.2 | 1.2
Day 6 | +0.9 | 1.6
Day 7 | +1.1 | 2.2 ← alarm
Change began day 4 (day after S was last 0). Alarm on day 7. Alarm date ≠ start date
Notes: Quiz: alarm date is not onset.

## Slide 10: The two knobs, set from σ
k = 0.5σ = 0.10 °C
Slack: ordinary noise does not pile up
h = 5σ = 1.02 °C
Decision limit: low = fast but noisy, high = calm but late
Notes: Both measured in sigma of the leftovers from 2024.

## Slide 11: CUSUM on the real amplifier (watching from Jan 2025)
With the yearly swing removed, this step is big, so CUSUM fires on day one
0.90
S the day before
2.86
S on 12 May 2025
1.02
h (5σ)
0 days
delay
Notes: CUSUM earns its keep on smaller faults: next slide.

## Slide 12: Practice: a +0.3 °C fault the point rule never sees
Leftovers: 0 hits above 3σ in 30 days
Chart: 
| 01 Jan | 10 Jan | 20 Jan | 01 Feb | 10 Feb | 20 Feb | 01 Mar
value | -0.332 | -0.066 | 0.102 | 0.135 | 0.173 | -0.23 | 0.156 | -0.209 | 0.016 | -0.031 | 0.087 | 0.175 | -0.281 | -0.289 | 0.064 | 0.085 | -0.029 | 0.113 | -0.119 | -0.298 | -0.155 | 0.027 | -0.186 | -0.219 | -0.128 | 0.082 | 0.267 | 0.248 | -0.094 | -0.046 | 0.023 | 0.185 | -0.162 | 0.092 | -0.08 | -0.274 | -0.319 | -0.219 | -0.279 | -0.165 | 0.345 | 0.421 | 0.241 | 0.608 | 0.431 | 0.289 | 0.492 | 0.275 | 0.111 | 0.269 | 0.202 | 0.583 | 0.083 | 0.183 | 0.547 | 0.163 | 0.599 | 0.565 | 0.096 | 0.487
CUSUM: alarm 13 Feb, start traced to 10 Feb
Chart: 
| 01 Jan | 10 Jan | 20 Jan | 01 Feb | 10 Feb | 20 Feb | 01 Mar
value | 0 | 0 | 0 | 0.034 | 0.105 | 0 | 0.054 | 0 | 0 | 0 | 0 | 0.073 | 0 | 0 | 0 | 0 | 0 | 0.012 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.165 | 0.312 | 0.116 | 0 | 0 | 0.083 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.243 | 0.563 | 0.702 | 1.208 | 1.538 | 1.725 | 2.115 | 2.288 | 2.298 | 2.466 | 2.567 | 3.048 | 3.03 | 3.111 | 3.557 | 3.619 | 4.117 | 4.58 | 4.574 | 4.959
Notes: The day after S was last zero is the start.

## Slide 13: Choosing h: fast and noisy, or calm and late?
h | False alarms | Caught after
2σ | 10 | 1 day
3σ | 1 | 2 days
5σ | 0 | 3 days
8σ | 0 | 5 days
10σ | 0 | 6 days
Same practice fault, 404 calm days. After an alarm is checked: reset S to 0
Notes: Pick h on purpose and write it down.

## Slide 14: The battery that's ageing faster
PART 2
The satellite's inverter for every eclipse
Notes: Section break.

## Slide 15: Battery capacity: a 95 Ah threshold fires 0 times
Chart: 
103.3 → 95.4 Ah, lowest 95.39. Use the week-04 file: the week-03 twin has no speed-up
Notes: Level never breaches.

## Slide 16: Not lower. Faster
Chart: 
| before April 2025 | after April 2025
Ah lost per year | 2.24 | 3.68
1.6× faster. No single day is unusual; the speed changed
Notes: The original quotes -2.4 and -4.0; the data says -2.24 and -3.68.

## Slide 17: Watch the speedometer: 90-day rolling slope
Chart: 
Crosses the −3.0 warning line on 2 May 2025: 31 days after the speed-up began
Notes: Trailing windows warn late.

## Slide 18: Right tool for each shape
Spike
point rule on the leftovers
Level shift
CUSUM on the leftovers
Drift / speed-up
rolling slope vs a warning line
Notes: Always remove what you already know first.

## Slide 19: Final project · Checkpoint 2: data in hand
Bring today
Unit head's reply; data loaded with .asfreq(); rows, range, gaps, duplicates; one honest plot
Data rules
Real NIGCOMSAT data stays on NIGCOMSAT systems (not Colab); no raw data on GitHub
Notes: Next checkpoint: Week 4 Day 3, method drafted.

## Slide 20: Your turn: 60 minutes
1
A: CUSUM by hand, write the one line
2
B: catch the amplifier's step + a secret fault
3
C: find when the battery started ageing faster
4
Bonus: how noisy is a jumpy h?
Notes: Walk the room.

## Slide 21: What you now know
A level shift can be huge locally yet invisible to a whole-series 3σ rule
CUSUM: S = max(0, S + leftover − k). Alarm date ≠ start date
Drift: watch the rolling slope, not the level
Next: Scoring a Detector + Quiz 2
Notes: Tease the answer key.