## Slide 1: When Will It Break? Remaining Useful Life + Quiz 4
WEEK 6 · DAY 2
Draw the trend, find the limit, and say when, honestly
Publica
Academy
Notes: Last teaching day: how long until a part reaches its limit? Then Quiz 4.

## Slide 2: Today's mission
Three shapes
how parts grow old
Draw the line
trend to threshold
Check the call
was the battery right?
Quiz 4
forecasting + remaining life
10 min hook · 30 min slides · 45 min hands-on · 20 min quiz · 15 min mark + wrap
Notes: Four moves.

## Slide 3: “Driver, fuel go reach Ojota?”
The danfo driver's sum
20 litres left ÷ 4 litres a trip = 5 trips (a story, not data)
That is remaining useful life
What's left above the limit ÷ how fast it's going. Fill up before the light comes on
Notes: RUL in one sum. Act before the crossing: Quiz 4 Q24.

## Slide 4: Remaining useful life is a national question
December 2011
NigComSat-1R launched to 42.5° East
15-year design life
2011 + 15 ≈ 2026
2028 · 2029
targets for NIGCOMSAT-2A and 2B
Notes: Facts from the toolkit fact sheet. Today's data is a synthetic teaching platform, not NigComSat-1R telemetry.

## Slide 5: Three ways to grow old
PART 1
One satellite, three parts, three limits
Notes: Section break.

## Slide 6: Same satellite, three shapes
Battery capacity
curves down, floor 80%: last reading 77.84%
Amplifier gain
straight, slow fade, floor −2 dB: last reading -0.783 dB
Propellant
steps at every burn, reserve 5 kg: last reading 101.93 kg
Notes: 1,825 days, 1 Jan 2021 – 30 Dec 2025. Limits are known up front, from degradation_thresholds.csv.

## Slide 7: Propellant: a staircase, not a slope
Station-keeping burns, counted in the five years of data
~14 days
between burns
0.39 kg
per burn (typical)
~26
burns a year
9.62 kg
used a year
Notes: Quiz 4 Q23. A straight line through a staircase is an approximation.

## Slide 8: Draw the line
PART 2
Fit the trend on the past, extend it to the limit
Notes: Section break.

## Slide 9: Trend-to-threshold: 3 years of battery data, line extended to 80%
Chart: 
Slope -4.59% a year. The line hits 80% on 1 May 2025: 486 days after the call on 1 Jan 2024.
Notes: Only the first three years are used, as if it were 1 Jan 2024.

## Slide 10: The whole method: fit_trend + day_of_threshold
x = np.arange(len(series))
slope, intercept = np.polyfit(x, series.values, 1)
line = np.poly1d([slope, intercept])
future = line(np.arange(len(series) + 4000))
crossed = future < threshold
day = np.argmax(crossed) # the FIRST True
np.polyfit(x, y, 1) → slope and intercept. np.argmax of True/False → position of the first True.
Notes: Quiz 4 Q20.

## Slide 11: The code book's calls, 3 years of data each
Two sensible dates and one strange one
1 May 2025
battery → 80%
5 May 2033
amplifier → −2 dB
1 Jan 2021
propellant → 5 kg ?!
Notes: 1 Jan 2021 is the first day of the data.

## Slide 12: The bug: np.argmax of “never” is 0
crossed = [False, False, False, False]
np.argmax(crossed) # 0 !!!
# FIXED in day_of_threshold:
if not crossed.any():
return None # "no crossing"
The line never reaches 5 kg before the search stops on 13 Dec 2034. Say “no crossing before 13 Dec 2034”, then look further.
Notes: A confident wrong date with no error. Check the 'nothing found' case.

## Slide 13: Propellant: the line gets there, just later
day = (5 − intercept) / slope → 6 Dec 2035
The 3-year line falls 9.72 kg a year and reaches the reserve about 12 years past the data it was fitted on.
Notes: A straight line can be solved for the crossing directly.

## Slide 14: The fuel-gauge sum agrees
101.93 kg
left on 30 Dec 2025
− 5 kg
de-orbit reserve
÷ 9.62 kg/yr
burned each year
10.1 years
≈ Jan 2036
The line said Dec 2035. Two methods, one story.
Notes: Simple sums are the best bug detectors.

## Slide 15: Was the battery call right?
PART 3
We have the next two years. Let's check
Notes: Section break.

## Slide 16: When did the battery “cross” 80%? Three honest answers
Daily readings bounce around the floor
14 May
① first day below 80%
20 Jun
② 30-day mean below 80%
24 Jul
③ last day at or above 80%
Notes: 49 of the 72 days in between are below 80%. A crossing is a window.

## Slide 17: The 3-year call (1 May 2025): early by how much?
①
13 days early
vs the first dip (14 May): the code book's answer
②
50 days early
vs the 30-day mean (20 Jun)
Notes: Define 'crossed' before you score. Quiz 4 Q29 uses the first dip.

## Slide 18: Backtest the method: the battery call from four starting points
Data used | Call made on | Predicted crossing | vs first dip | vs 30-day mean | Warning
1 year | 1 Jan 2022 | 1 Mar 2025 | -74 d | -111 d | 1,229 d
2 years | 1 Jan 2023 | 7 Apr 2025 | -37 d | -74 d | 864 d
3 years | 1 Jan 2024 | 1 May 2025 | -13 d | -50 d | 499 d
4 years | 31 Dec 2024 | 18 May 2025 | +4 d | -33 d | 134 d
More data → closer call, but less warning. Against the 30-day mean, every call is early.
Notes: Quiz 4 Q30.

## Slide 19: Why early? The fade is slowing down (% a year)
Chart: 
| 2021 | 2022 | 2023 | 2024 | 2025
value | 4.81 | 4.69 | 4.55 | 4.45 | 4.34
A line fitted on the early, faster years overstates the later fade. Early is the safe side for a battery.
Notes: Capacity lost per year, from a line through each calendar year.

## Slide 20: The battery ages when it works
Eclipse seasons: 27 Feb – 13 Apr and 1 Sep – 16 Oct
24.7%
of the days are eclipse days
43.4%
of all the fade happens on them
2.3×
faster per day than in sunlight
Notes: Batteries wear out by charging and discharging, which only happens in the shadow.

## Slide 21: The long reach: calls from 1 to 5 years of data
Data used | Amplifier → −2 dB | Propellant → 5 kg
1 year | 27 Nov 2033 | 23 Oct 2035
2 years | 26 Jul 2033 | 13 Dec 2035
3 years | 4 May 2033 | 6 Dec 2035
4 years | 17 Mar 2033 | 14 Dec 2035
5 years | 24 Mar 2033 | 15 Dec 2035
Amplifier: around 2033, calls span ~8 months. Propellant: within 53 days, if the burn plan holds; fuel-gauge sum Jan 2036.
Notes: Quiz 4 Q22: a planning figure with a range, re-estimated every year.

## Slide 22: Golden rules for remaining useful life
1
Report a window, never a single day
2
Say how far past the data you reach
3
Act before the crossing, and re-estimate regularly
4
“No crossing” is an answer, not day 0
Notes: Battery: dips below 80% mid-May 2025, below for good by late July. Amplifier: around 2033, re-check yearly. Propellant: late 2035 to early 2036 if the burn plan holds.

## Slide 23: Quiz 4: 30 questions, 20 minutes
1
Phones down, notebooks closed, no AI
2
Circle one letter per question
3
Answers are spread across A–D: no “always B”
4
Swap papers and mark together
Notes: Use the PDF or the Google Forms CSV.

## Slide 24: Your turn: 45 minutes
1
Open W6D2-exercise, save a copy, run STEP 0
2
Part A: draw the line, find the bug, do the fuel sum
3
Part B: check the battery call from 4 starting points
4
Part C: eclipse ageing, the long reach, the honest report
Notes: Walk the room.

## Slide 25: What you now know
RUL = extend the trend until it crosses the known limit; check “no crossing” honestly
Backtest the method from several starting points, with “crossed” defined first
Report a window, say how far you reach, act before the crossing, re-estimate
Next: Project clinic & demo day · bring your tool, report and honest test table
Notes: Recap.